## Slide 1: Genetec CCTV End-User Training Searching Video Overview
Presented by:

## Slide 2: Table of Contents
Genetec CCTV End-User Training
Searching Video Overview
July 2019 / 5.7 version / 2
What are the ways I can search past video? Slide 3
How do I search past video by date/time and camera(s)? Slides 4 - 7
How do I search past video for motion? Slides 8 - 11
How do I search past video for a specific area? Slides 12 - 16
How do I search past video for bookmarks? Slides 17 – 18
Additional Resources Slide 19

## Slide 3: What are the ways I can search past video?
July 2019 / 5.7 version / 3
  The most commonly-used search parameters and the associated Security Desk task for each parameter are shown below:
    Date and time
    Camera(s)
    Motion
  Targeted area
  Bookmarks

## Slide 4
July 2019 / 5.7 version / 4
From the Archives task, select a camera
Select a time period by either
  Choosing the tab “All Available” and selecting one of the days displayed
  OR
  Choosing the tab “Time range” and manually specifying the time period
How do I search past video by date/time and camera(s)?

## Slide 5
July 2019 / 5.7 version / 5
Click the “Generate report” green button at the bottom.
The report results will display all available video in one-hour increments.
For easier viewing of report results, drag the “….” down to shrink the canvas.
How do I search past video by date/time and camera(s)?

## Slide 6
July 2019 / 5.7 version / 6
To view any of the report results simply drag it into one of the canvas tiles.
How do I search past video by date/time and camera(s)?

## Slide 7
July 2019 / 5.7 version / 7
If you’d like to export any of the video sequences, simply select the desired line item(s) from the report results and click on the “Export video” icon in the lower left corner of the report results.
How do I search past video by date/time and camera(s)?

## Slide 8: How do I search past video for motion?
July 2019 / 5.7 version / 8
From the Motion Search task, select camera(s) by opening the camera drop down menu at the top of the screen.
If the camera you selected does not support motion search functionality you will receive the following message.

## Slide 9: How do I search past video for motion?
July 2019 / 5.7 version / 9
Select a time range for your search by either specifying how many days or which dates/times you would like to search.
OR

## Slide 10: How do I search past video for motion?
July 2019 / 5.7 version / 10
Use the icons below the preview image to define the motion detection zone
Fill tool: Defines the motion detection zone as the entire image
Rectangle tool: Allows you to draw a rectangle to determine motion detection zone.
Eraser tool: Allows you to erases specific previously drawn motion detection zones.
Clear All tool: Clears all previously drawn motion detection zones.

## Slide 11: How do I search past video for motion?
July 2019 / 5.7 version / 11
You may influence the speed and accuracy of the motion detection search by altering the following parameters:
  Motion threshold: The higher the number the more motion required to appear in the report results.
  Consecutive frame hits: The higher the number the more frames that must contain motion to appear in the report results.
  Minimum time between frames: The higher the value, the more frames the system skips during the search process and the faster (but less accurate) the search process becomes. To examine every frame, set value to 33 ms or less.
Click on the green button at the bottom “Generate report”.

## Slide 12: How do I search past video for a specific area?
July 2019 / 5.7 version / 12
If you know which camera recorded a specific event and a time when it might have taken place, you can search past video for the event.
From the Monitoring task, drag the desired camera into a tile on the canvas.
Make sure the tile is selected (indicated by a yellow border around the outside of the tile)

## Slide 13: How do I search past video for a specific area?
July 2019 / 5.7 version / 13
Click on the “Quick search” icon on the dashboard.
In the Quick search pop up window, use your mouse to draw a rectangle around the area you want to search.
Click Start.

## Slide 14: How do I search past video for a specific area?
July 2019 / 5.7 version / 14
An overview of the last six hours of video recording will be displayed in a series of thumbnails focused on just the area you selected.
To isolate what time this car left its parking spot, click several times on the magnifying glass icon to narrow down the time period.
Thanks to the Quick search feature we have determined the car left the parking spot at 5:10 PM.

## Slide 15: How do I search past video for a specific area?
July 2019 / 5.7 version / 15
To view the video associated with the car leaving its spot, simply click on the thumbnail and the corresponding video will being playing in the canvas.

## Slide 16: How do I search past video for a specific area?
July 2019 / 5.7 version / 16
Once a video is playing in the canvas, you can right click on the tile and click on “Camera” to access the following common options:
  Add a bookmark
  Save a snapshot
  Export video

## Slide 17: How do I search past video for bookmarks?
July 2019 / 5.7 version / 17
  From the Bookmarks task, select search parameters such as camera(s), message and time range.
  Click on the green button at the bottom labeled “Generate report”.

## Slide 18: How do I search past video for bookmarks?
July 2019 / 5.7 version / 18
  From the report results pane above the canvas, select the Bookmark you would like to view.
  Drag the line item into one of the tiles for viewing.
  The bookmark is notated in the timeline at the bottom of the video.
  You can also delete, export or edit any of the bookmarks by clicking on the icons in the bottom left of the report results pane.

## Slide 19: Additional Resources
July 2019 / 5.7 version / 19
For additional resources on how to get the most out of your security system, please visit our website at:
www.jmgsecurity.com
Additional PowerPoint training guides are available from JMG on topics such as overview of Security Desk, viewing live video and searching recorded video. To request any of these, please contact JMG at 800-900-4564.